## Slide 1: ANNUAL MEETING RERC on Technologies for Children with Orthopedic Disabilities NIDRR H133E100007
Program Director: Gerald F. Harris, Ph.D., P.E.
Program Co-Director: Li-Qun Zhang, Ph.D.

## Slide 2: Project R2 Annual Update R2: Diffusion Tensor Imaging and Restoration of Upper and Lower Limb Function in Children with Cerebral Palsy
Dr. Brian Schmit & Dr. Michelle Johnson

## Slide 3: R2A: Diffusion Tensor Imaging and Restoration of Upper and Lower Limb Function in Children with Cerebral Palsy
Cerebral Palsy (CP)
Subject population: 20 CP, 10 typical children
Overall goal
  Quantitatively assess brain white matter structure (DTI and fMRI) before and after combined intervention strategies of surgery plus novel robot therapies

## Slide 4: R2A Lower Extremity (LE) Hypotheses
The motor adaptations to hamstring lengthening depend on the underlying structure of the brain white matter tracts, (e.g. corticospinal tracts and thalamic radiations) as measured using DTI
fMRI measures of brain plasticity will reflect the extent of motor adaptation to hamstring lengthening transfers
Robotic interventions will accelerate fMRI changes as well as subsequent recovery of motor function

## Slide 5: R2A – LE Specific Aims
Predict neural adaptations to orthopedic treatments for CP using DTI measures of brain structure
Characterize brain plasticity in response to combined orthopedic and novel robotic interventions

## Slide 6: R2A – LE Procedures
Algorithm Development
Develop a voxel-wise analysis approach to characterize overall differences in brain structure.
Test approach in existing data.

## Slide 7: R2A – LE Procedures
Imaging in Controls
Program Scanner for image sequence
Test scanner for image quality
  Post-hoc adjustments for artifacts
Verify fMRI during pedaling
Validate DTI metrics in brain gray and white matter.

## Slide 8: R2A LE Time Line
Activity: | Year 1 | Year 2 | Year 3 | Year 4 | Year 5
Adapt Imaging Techniques |  |  |  |  | 
Adapt Robotic Intervention Techniques |  |  |  |  | 
Finalize experimental set-up |  |  |  |  | 
Subject recruitment |  |  |  |  | 
Data collection in typical children |  |  |  |  | 
Data collection in CP children |  |  |  |  | 
Data Analysis |  |  |  |  | 
Publications |  |  |  |  | 

## Slide 9: R2A – LE Progress
New Algorithm for classifying brain structure – Voxelwise Indirect Structural Connectivity

## Slide 10: R2A LE Progress
Coil Artifact Correction

## Slide 11: R2A - LE Progress
fMRI Validation
Able to measure fMRI during pedaling in controls

## Slide 12: R2A LE Progress
Validation of DTI metrics in controls

## Slide 13: R2A LE Progress
Labeling individual white matter tracts

## Slide 14: R2A LE Accomplishments
Accomplishments
  Imaging techniques developed and validated
  4 control subjects
Publications
  Voxelwise Indirect Structural Connectivity in preparation

## Slide 15: R2A LE Opportunities
Publication of control DTI and VISC in children
Use DTI to predict gait function (nonsurgical)

## Slide 16: Plans for Year 3
Collect data in CP children

## Slide 17: R2B: Diffusion Tensor Imaging and Restoration of Upper and Lower Limb Function in Children with Cerebral Palsy
Dr. Michelle Johnson

## Slide 18: R2B: DTI and Restoration of Upper and Lower Limb Function in Children with Cerebral Palsy – Annual Report 2012
Cerebral Palsy (CP)
Subject population: 20 CP, 10 typical children
Overall goal
  Quantitatively assess brain white matter structure (DTI and fMRI) before and after combined intervention strategies of surgery plus novel robot therapies

## Slide 19: R2B Upper Extremity (UE) Hypotheses
The motor adaptations to wrist tendon transfers depend on the underlying structure of the brain white matter tracts, (e.g. corticospinal tracts and thalamic radiations) as measured using DTI
fMRI measures of brain plasticity will reflect the extent of motor adaptation to wrist tendon transfers
Robotic interventions will accelerate fMRI changes as well as subsequent recovery of motor function

## Slide 20: R2B – UE Specific Aims
Predict neural adaptations to orthopedic treatments for CP using DTI measures of brain structure
Characterize brain plasticity in response to combined orthopedic and novel robotic interventions

## Slide 21: R2B – Aim 1 UE Procedures/Tasks
Complete MRI compatible glove for children
Scan 20 Health Children
  Diffusion Tensor Imaging (DTI), Spoiled Gradient Echo (SPGR), Grasp Tasks (2 trials)/Reach Tasks(2 trials)
Accomplishment: Glove Completed; 10 Healthy Child Subjects Scanned

## Slide 22: Building the Glove
I used the adult glove as reference
Learned to solder, and spliced wires
4 sensors were used to calculate grasp aperture
Subjects wore the glove, their grasp aperture was reflected as a circle
They had to close the hand to the smaller circle
sensor 3
sensor 4
cable strap
sensor 1
sensor 2
sensor cable
Finger Measurements
Notes: Li1=Index MCP PIP
Li2=Index PIPTIP
Lt1=Thumb MCPPIP
Lt2=Thumb PIPTIP
D=distance Index MCP Thumb MCP
Tip to tip is the grasp aperature

## Slide 23: MRI Scanner
1.
5.
4.
3.
2.
Notes: Four scans were completed in a 3.0T GE MRI Scanner
MRI is a way for us to see inside your body
The MRI we use is only for research purposes, not the kind used for diagnosis and treatment

## Slide 24: R2B – UE Preliminary Results
Analyzed 7 Children
Determined fMRI Activation
Mean activations on left in three regions were greater than on right
Mostly contralateral laterality indexes
The healthy children who used their right hand to complete the grasping tasks used the left side of their brains to execute movements
Chart: Mean Activation of Normal Subjects
| left_S1_ML | right_S1_ML | left_M1_ML | right_M1_ML | Left_BA6 | Right_BA6
 | 2.2787 | 0.57457 | 1.4637 | 0.51762 | 1.4877 | 0.45657
Chart: Lateral Index
| M1 | S1 | BA6
normal | 0.44536 | 0.35141 | 0.46154

## Slide 25
R2B – Aim 2 UE Procedures/Tasks
Complete Robot Hardware Design
Complete Robot Orthosis Design
Complete Robot Software and Control Program
Accomplishment: Hardware designs are completed and 90% implemented. Software designs are completed and 25% completed.

## Slide 26: R2B - UE Robot/Orthosis
Passive follower
Robot
Active Robot
( for Impair arm)
Experimenter
Station
Target PC and
Electronic
Box

## Slide 27: R2B UE Time Line
Activity: | Year 1 | Year 2 | Year 3 | Year 4 | Year 5
Adapt Imaging Techniques |  |  |  |  | 
Develop upper limb robot and Adapt Robotic Intervention Techniques |  |  |  |  | 
Finalize experimental set-up |  |  |  |  | 
Subject recruitment |  |  |  |  | 
Data collection in typical children |  |  |  |  | 
Data collection in CP children |  |  |  |  | 
Data Analysis |  |  |  |  | 
Publications |  |  |  |  | 

## Slide 28: R2B UE Progress
10 typical children tested and Scanned
Next Steps:
  Collect remaining 10 healthy children
  Conference paper based on fMRI/DTI results
  Recruit and test and train CP children